## Slide 1: Chengdu AV-EV Engineering Center: Battery Management System Development Simcenter Engineering and Consulting, 06/05/2020
Realize Innovation
June 2020

## Slide 2: Document Outline
Project Overview and Introduction to BMS
BMS Development V Diagram
BMS Architecture
Polarion for System Engineering
BMS Development 1: Control Dev and Open Loop Testing
BMS Development 2: Model based Closed Loop Testing
BMS Development 3.: Software in the Loop Testing
BMS Development 4.: RPC Testing with Labjack

## Slide 3: Project Overview Project Context and Target
Setup end-to-end workflow to demonstrate the development of Battery Management System (BMS) algorithms and software on a virtual battery pack
      Process orchestration using Polarion
      Requirements and Test Cases organization and management using Polarion
      Battery cell and pack models implemented in Simcenter Amesim to test and verify the BMS algorithm and software
      BMS algorithms implemented as control logic in MATLAB/Simulink and its verification testing executed using MIL simulation
      Embedded application C-code generated from the algorithm model using auto code generation technology and SIL based tests executed to verify functionality.
Implement the developed BMS algorithm software on a Rapid Prototyping Electronic Control Unit (RPC)
      This BMS controller can be used on the HIL bench planned for the second phase of the BMS demonstrator.

## Slide 4: BMS System Closed Loop Overview
ECU
Micro Processor
Embedded Software
I/O Hardware
sensor
actuators
Battery Pack (Plant)
Controller
Vehicle Commands
  Objectives: Control system is required to
    Monitor pack current, voltages, temperatures
    Control battery temperature to desired range
    Determine state of charge and available energy (fuel gauge), state of health and power limits
    Keep cells within safe operating ranges to prevent damage and abuse and prolong the cell life
    Fulfill functional requirements of the application in which it is used

## Slide 5: MBSE Development Process for BMS
Requirements analysis
Algorithm Specification development
Model based algorithm testing
(MIL)
ECU System integration bench testing
Powertrain system testing
Vehicle integration & testing
Code-generation
Architecture Partitioning
ECU Requirements and Change Requests
Different levels of plant models to test different control features
Style Guides, Blocksets and Style Checkers
Open-Loop & Closed-Loop Testing; Automated Testing
Coverage based Test Quality enhancements
Integration with legacy C-code for application build
Repeat Open-Loop & Closed-Loop Testing; Automated Testing
More effort spent upstream to reduce later re-work
MIL
SIL
HIL
ESD

## Slide 6: BMS System Architecture
Hardware Layer
Low-Level Drivers
Virtual I/O Layer
I/O Layer
Battery Management System Layer (Software Features)
Software
Battery V-I-T Monitoring and Diagnostics
Contactor Control
Low Voltage Battery Control (cell balancing)
Thermal controller
State and Mode Control
Low-Level Drivers
Virtual RTOS Layer
RTOS Layer
SOC
SOP
SOH

## Slide 7: Managing the Software Development Artifacts Polarion for BMS Development
Siemens utilized Polarion ALM during the development of the Battery Management System
Utilizing Polarion ALM allowed software engineers the ability to efficiently manage software development artifacts, maintain detailed traceability between artifacts, and quickly conduct impact analysis across the application.
Development artifacts stored in Polarion
Polarion application level: software dev status, solved/in progress issues tracking, etc
Polarion software feature level: high level functional document, requirements, test cases, Simulink model, test results, issues tracking, etc

## Slide 8: BMS Development Step 1: Simulink model development and Open Loop Testing
Create Simulink model for each BMS feature according to high level feature functionality document
Create open loop testing harness for open loop testing of each feature
  Requirements define various test cases associated with each feature
  Test cases will be used to generate appropriate inputs for open loop testing
Open Loop Testing Harness (SOP)
Simulink model for State of Power (SOP)
Requirements
Test Cases
Test Results
Functional High Level Documentation
Example :Discharging power limit
and current limit

## Slide 9: Amesim Battery Model for MIL and SIL
Power cycle Input
Contactor model:
Precharge contactor
Main contactor
Charger contactor
Amesim/Simulink Interface
Battery pack model
Battery model in Simulink

## Slide 10: BMS Development Step 2: Simulink model Closed Loop Testing with Amesim Battery Model
Amesim Battery Model
BMS
Data Logger
Key and Charger Signals
Feedback Displays
10 test cases for closed loop testing

## Slide 11: BMS Development Step 3: Software in the Loop Testing with Amesim Battery Model
10 test cases for SIL testing
Software in the Loop Testing in Simulink Environment
Amesim Battery Model
BMS Simulink
Code
Test results compare with
Simulink Code results

## Slide 12: BMS Development Step 4: Rapid Prototyping Control (RPC) Unit Testing Setup
Laptop computer for development & communication
CAN Communication
RPC: PI Innovo M110
Power supply
USB connection
Analog/Digital connection
Labjack signal generator board
Labjack can generate analog, digital, and CAN signals like a battery pack for open loop testing of RPC
RPC contains 3 CAN channels and multiple analog/digital pins suitable for BMS application
PC can be used for code generation and flashing/logging RPC, and download signals to Labjack boards
Testing Results Example

## Slide 13: Thank You
Realize innovation.
Restricted © Siemens AG 2019